## Slide 1: SCSA1201 FUNDAMENTAL OF DIGITAL SYSTEMS
Unit – 4
SEQUENTIAL CIRCUITS

## Slide 2: Syllabus
UNIT III SEQUENTIAL CIRCUITS
Introduction to Sequential circuits – Flip flops – SR, JK, D and T flip flops, Master Slave flip flop, Characteristic and excitation table – Realization of one flip flop with other flip flops – Registers – Shift registers – Counters – Synchronous and Asynchronous counters – Modulus counters – Ring Counter – Johnson Counter – State diagram, State table, State minimization – Hazards

## Slide 3: Sequential Circuits
The outputs of sequential circuit depends not only on the combination of present inputs but also on the previous outputs.

## Slide 4: Types of Sequential Circuits
Asynchronous sequential circuits : In asynchronous sequential circuits change in input signals can affect memory element at any instant of time.
Synchronous sequential circuits : In Synchronous sequential circuits, signals can affect the memory elements only at discrete instants of time.

## Slide 5
The Comparison Between Combinational and Sequential Circuits

## Slide 6
Classification of Logic Circuits

## Slide 7: Comparison Between Synchronous and Asynchronous Sequential Circuits

## Slide 8: Clock Signal
A clock signal is a particular type of signal that oscillates between a high and a low state. It is produced by clock generator.
Types of Triggering
Level triggering
Edge triggering

## Slide 9: Level triggering
Positive level triggering- If the sequential circuit is operated with the clock signal when it is in Logic High, then that type of triggering is known as Positive level triggering
Negative level triggering- If the sequential circuit is operated with the clock signal when it is in Logic Low, then that type of triggering is known as Negative level triggering.

## Slide 10: Edge triggering
Positive edge triggering - If the sequential circuit is operated with the clock signal that is transitioning from Logic Low to Logic High, then this is known as Positive edge triggering
Negative edge triggering - If the sequential circuit is operated with the clock signal that is transitioning from Logic High to Logic Low, then this is known as Negative edge triggering

## Slide 11: LATCHES and FLIP FLOPS
A flip-flop or latch is a circuit that has two stable states and can be used to store one bit either 0 or 1.
The main difference between latches and flip-flops is that, latches operate with enable signal, which is level sensitive whereas, flip-flops are edge sensitive.
Types of flipflop
1.SR Flipflop
2.D Flipflop
3. JK Flipflop
4. T flipflop

## Slide 12: Bi-Stable Element

## Slide 13: Clocked SR Flipflop (Set-Reset Flipflop)
Logic Symbol
Logic Diagram

## Slide 14: Clocked SR Flipflop Working
Case1: When S=R=0, clk=1,Qn=0,
Case1: When S=R=0, clk=1,Qn=1,
Qn+1=0 same as previous output
Qn+1=1 same as previous output

## Slide 15: Clocked SR Flipflop Working Contd..
Case2: When S=0; R=1, clk=1, Qn=0,
Case 2: When S=0; R=1, clk=1, Qn=1
Qn+1= 0 Reset
Qn+1 = 0 Reset

## Slide 16: Clocked SR Flipflop Working Cont..
Case 3: When S=1; R=0, clk=1, Qn=0,
Case 3: When S=1; R=0, clk=1, Qn=1
Qn+1= 1 Set
Qn+1 = 1 Set

## Slide 17: Clocked SR Flipflop Working Cont..
Case 4: When S=1; R=1, clk=1, Qn=0,
Case 4: When S=1; R=1, clk=1, Qn=1
Qn+1= 1 & Q’n+1 is also one which is an indeterminate state
Qn+1= 1 & Q’n+1 is also one which is an indeterminate state

## Slide 18: Clocked SR Flipflop Working Contd..
Case 1: If S=R=0 and the clock pulse is applied, the output do not change, Qn+1 = Qn
Case 2: If S= 0, R=1 and the clock pulse is applied, Qn+1= 0
Case 3: If S= 1, R=0 and the clock pulse is applied, Qn+1= 1
Case4: If S= 1, R=1 and the clock pulse is applied, the state of the flipflop is undefined.

## Slide 19: Clocked SR Flipflop Working Contd..
Qn+1 = S+ R’Qn
Characteristic Equation

## Slide 20: D Flipflop
The modified SR flipflop is known as delay flipflop (D Flipflop).
D input is connected to S input and complement of D input is connected to R input of SR flipflop.
Logic symbol

## Slide 21: D Flipflop working cont…
Characteristic table
( i) When D=1, S=1 and R=0 ; the output is set
(ii) When D=0, S=0 and R=1 ; the output is reset
Logic Diagram
Excitation table
State diagram
Characteristic Equation
Qn+1 = D

## Slide 22: JK Flipflop
JK flipflop is also a modification of SR flipflop.
The uncertainity in the state of an SR flipflop when S=R=1 is being eliminated in JK flipflop.
Logic symbol

## Slide 23: JK Flipflop working cont…
Logic Diagram
J input is ANDed with Q’ to obtain S input and K input is ANDed with Q to obtain R input.
Thus S= J.Q’ and R= K.Q.
Case 4: J=1 and K=1
Q=0, Q’=1 : When J=1 ,K=1 and Q=0; S=1 and R=0 then Qn+1=1.
Q=1, Q’=0 : When J=1 ,K=1 and Q=1; S=0 and R=1 then Qn+1=0
Hence, when J=1 and K=1 ; Qn+1= Qn’(Toggle)
Case 3: J=1 and K=0
Q=0, Q’=1 : When J=1 ,K=0 and Q=0; S=1 and R=0 then Qn+1=1.
Q=1, Q’=0 : When J=1 ,K=0 and Q=1; S=0 and R=0 then Qn+1=1.
Hence, when J=1 and K=0 ; Qn+1= 1 (Set)
Case 2: J=0 and K=1
Q=0, Q’=1 : When J=0 ,K=1 and Q=0; S=0 and R=0 then Qn+1=0.
Q=1, Q’=0 : When J=0 ,K=1 and Q=1; S=0 and R=1 then Qn+1=0.
Hence, when J=0 and K=1; Qn+1= 0(Reset)
Case 1: J=K=0
When J=K=0, S=R=0 and according to truth table of SR flipflop, output does not change. Hence,
when J=K=0; Qn+1= Qn (no output change)

## Slide 24: JK Flipflop working cont…
Characteristic table
Excitation table
State diagram
Characteristic Equation
Qn+1 = JQn’ +K’Qn

## Slide 25: T Flipflop
T Flipflop is also known as toggle flipflop. It is a modification of JK flipflop
T Flipflop is obtained from a JK flipflop by connecting both inputs, J and K together
Logic symbol

## Slide 26: T Flipflop working contd…
Characteristic table
When T=0, J=K=0 and hence
Qn+1= Qn (no output change)
(ii)When T=1, J=K=1 and hence Qn+1= Qn’ (toggles)
Logic Diagram
Excitation table
State diagram
Characteristic Equation
Qn+1 = TQn’ +T’Qn

## Slide 27: Master slave Flipflop
In master slave JK flip flop, it consists of clocked JK flipflop as a master and clocked SR flipflop as a slave.
The output of master flipflop is fed as an input to the slave flipflop.
Clock signal is directly connected to the master flipflop and it is connected through inverter to the slave flipflop
During the positive clock pulse, the information present at the J & K inputs is transmited to the output of master flipflop and it is held there until the negative clock pulse occurs.
After which it is allowed to pass through the output of slave flipflop.
Logic symbol
Logic Diagram

## Slide 28: Master slave Flipflop
When J=0, K=0,output of master remains same at the positive clock and the output of slave also remains same at the negative clock.
When J=0, K=1,output of master resets at the positive clock and the output of slave also resets at the negative clock.
When J=1, K=0,output of master sets at the positive clock and the output of slave also sets at the negative clock.
When J=1, K=1,output of master toggles at the positive clock and the slave then copies the output of master at the negative clock. This prevents race around condition.
[In JK flip flop as long as clock is high for the input conditions J&K equals to the output changes or complements its output from 1–>0 and 0–>1.This is known as race around condition.]
Logic Diagram
Truth Table

## Slide 29: Excitation Table or Application Table

## Slide 30
Realization of One Flip - Flop using Other Flip - Flops

## Slide 38: Excitation Table or Application Table

## Slide 39: Registers
Registers are groups of flip-flops , where each flip-flop is capable of storing one bit of information. An n-bit register is a group of n flip-flops. The basic function of a register is to hold information in a digital system and make it available to the logic elements for the computing process.
A register consists of a collection of binary storage cells, each implemented by a flip-flop. The number of cells determines the length of the register and, therefore, the length of the binary word stored within the register.

## Slide 40: Types of Registers in CPU
Accumulator ( Acc) : This is the most frequently used register used to store data taken from memory.
Memory Address Registers (MAR): It holds the address of the location to be accessed from memory.
Memory Data Registers (MDR): A register used for holding information (either program words or data words) that is in the process of being transferred from the memory to the central processor, or vice versa.
General Purpose Registers ( GPS) : The general purpose registers are used to store temporary data in the time of different operations in microprocessor.
Program Counter (PC): A program counter is a register in a computer processor that contains the address (location) of the instruction being executed at the current time.
Instruction Register (IR): In computing, the instruction register (IR) or current instruction register (CIR) is the part of a CPU's control unit that holds the instruction currently being executed or decoded.

## Slide 41: Shift Registers
Shift Registers are used for data storage or for the movement of data and are therefore commonly used inside calculators or computers to store data such as two binary numbers before they are added together, or to convert the data from either a serial to parallel or parallel to serial format.

## Slide 42: Shift Registers Cont..

## Slide 43: Shift Registers cont..

## Slide 44: Type of Shifting Operation in Shift Registers

## Slide 45: Mode of operation in Shift Registers

## Slide 46: Types of Shift Registers

## Slide 54: Counters

## Slide 55: Types of Counters

## Slide 56: Comparison Between Asynchronous and Synchronous Counters

## Slide 58
Cont..

## Slide 59
Cont..

## Slide 60
Cont..

## Slide 61
Cont..
Cont..

## Slide 63: Cont..

## Slide 66: Cont..
Operation

## Slide 68
Operation
Cont...

## Slide 73: MOD ( Modulus) Counter
Flip-Flops can be connected together to perform counting operations. Such a group of Flip- Flops is a counter. The number of Flip-Flops used and the way in which they are connected determine the number of states (called the modulus) and also the specific sequence of states that the counter goes through during each complete cycle.

## Slide 75: Design of Asynchronous MOD Counter
Procedure

## Slide 76: Asynchronous BCD counter or MOD- 10 counter
Count from 0 – 9 ( 0000 – 1001)
From 10 – 15 ( 1010 – 1111) Reset

## Slide 77
BCD counter or MOD- 10 counter

## Slide 78: Design of Synchronous MOD Counter

## Slide 79: Design of Synchronous MOD Counter Cont..
Step 4: Simplification using K - Map

## Slide 80: Design of Synchronous MOD Counter Cont..
Step 5: Draw the Logic diagram

## Slide 81: Ring Counter
6 – bit Ring Counter circuit Diagram
Truth Table
State Diagram
Count = Number of flipflops
Used to identify the active state with Logic 1

## Slide 82: Johnson Counter
Circuit Diagram
Truth Table
Count = Number of Flipflops * 2
Reduce the Number of Flipflops